## Slide 1: SensoStep Plantar Pressure Sensor
Final Project: Cornerstone of Engineering
Angela Gross, Sally Dorer, Tori Christianson, Emaan Jivani, Mohak Kothari

## Slide 2: Why this product?
We wanted to create an analysis tool device for those with issues in their feet to watch the pressure in their foot due to various medical/athletic reasonings
  Could be used by powerlifters(squat) to check pressure across foot for optimal performance or runners to check the pressure depending on how they strike when running.
  If you have a limp, trouble balancing, or other plantar issues, our goal is for SensoStep to help make them clear to understand and get the help you need.

## Slide 3
Overuse Injuries
Achilles tendinopathy – pain swelling impaired function
Shin splints – periostitis along the medial tibia
Caused by increased pressure in the deep posterior compartment of the leg

## Slide 4: Flat Footedness
Flat footedness can lead to muscle imbalances, and degenerative effects of the lower limb and spine
Increased risk of injury/pain from activity  can lead to decreased activity
Risk factors: family history, BMI over 30, urban residence, the use of footwear in infancy, age, being male

## Slide 5: Our Sensors: Force Sensing Resistor
Invented 1977
Comprised of an active area and a conductive area
Pressure changes resistance  sensor outputs data
Hex – representation of sensor data using base 16 numbering

## Slide 6: Inserting Wires
Wiring components are protected by hard plastics, leaving only the sensors pads on the outside
  Keeps pressure off delicate components
Allows for the wires to travel through the sole without the user feeling
Organizes wires - All wires come out in the same area

## Slide 7: Wire Box

## Slide 8: Data Collection- ArduinoBLE
BLE- "Bluetooth Low Energy"
  Optimal for low data processing and best option for our project, as the data that we are receiving is not that complex

## Slide 9
Final Circuitry Assembly
Using resistance pressure sensors, which provide a direct reading of the pressure on a scale of 0 to 1024 (bytes), which is better for the following reasons:
  #1: They plot much smoother
  #2: They are much more sensitive and accurate
  #3: They are flexible and versatile, not easily broken unlike the piezo sensors we opted for before
Measuring each sensor output via analog A1-A5, then via bluetooth

## Slide 10: ArduinoBLE
ArduinoBLE- purchased from Arduino website for $26.30
  Uses Bluetooth to communicate with each of the sensor inputs
    Requires power, which will be resolved with a portable charger with USB port
      Issues encountered where the circuit does not draw enough power to keep the battery on and turns off in ~90 seconds.

## Slide 11: Programming the ArduinoBLE
Declaring/Creating the ArduinoBLE SERVICE
Declaring/Creating the ArdunioBLE CHARACTERISTICS with universal unique identifiers (UUIDS)
Setting up the Serial Monitor and starting the ArdunioBLE, also adding a condition if it fails to start up
Adding all the declared CHARACTERISTICS to the declared SERVICE, and then ADVERTISING the service (making it be seen publicly)

## Slide 12: Connecting to Generic Bluetooth App
Since the BLE is advertising, any generic Bluetooth app will be able to pick it up and connect to it
  Must enable NOTIFICATIONS (data values will change with new info) every time it is used, and the display value has to be changed from hex to decimal
  While this method does receive our data, we wanted an easier and clearer way of displaying our data

## Slide 13: Connecting to Python
Imported 2 libraries into Python to interpret the data:
  Simplepyble
    Related to the ArduinoBLE, taking in its information
  Matplotlib.pyplot
    Actual live plotting of the points as seen on the left
Ran Python script through command prompt, selected relevant Bluetooth device (in this case #20, but varies per scan

## Slide 14
Sally – Average height arch
Angela – flat feet (near equal pressure across the foot)
Tori – high arches (arch sensor not activated)
Emaan – feet too small, heel sensor barely activated

## Slide 15: Walking Data Collection

## Slide 16: Additional Data- Walking
^Sally's Walking Pattern ^
^Angela's Walking Pattern ^
Tori's Walking Pattern
High arch height
= estimated arch reading average
~775
~815
~615
Normal arch height
Low arch height (flat feet)

## Slide 17
Connecting to the “App”
Done:
  Used Python and Tkinter/CustomTkinter libraries to create a highly simplified app interface as shown on the right.
  The graph that updates the pressure output was created using python, Arduino Nano 33 BLE integration using the matpylib and simplepyble libraries
Challenges:
  The only issue was when the graph was run, the original python script from the previous slide would pop up along with the embedded graph in the app

## Slide 18: Conclusion
Challenges:
  We need a battery pack that effectively draws enough power to allow the product to stay connected for a longer period.
  The app does need some refining to remove the pop-up when the graph starts plotting for a better user experience
  Convert bites to more widely know unit
  Display ratios between sensors instead of only a graph
  Clunky/large apparatus to hold the wiring/battery
  User-friendly interface à convert bites to a more common unit, calculate ratios between different sensors instead of displaying graph
Overall:
  SensoStep did the job we set out for it to do, to track pressure distribution
    This device can help understand a lot about a person’s foot and lower limb health
    If we continued working on it, we would make the device more comfortable/easy to wear and set up because that is a very large selling point if put on the market

## Slide 19
Material Cost
Materials | Cost
Sole Pad | $8.49
Sparkfun Kit | $99.95
Shoe | $10.00
Arduino Nano 33 BLE | $26.30
Leg Strap | $10.00
Sensors (5) | $10.00
Total Cost: $164.74

## Slide 20
Thank you, any questions?